## Slide 1
A technical deep dive into Intel CET
Implementation in Linux
Jay Tharwani, NetApp Inc.

## Slide 2
What We'll Cover
01
The Problem: ROP & JOP Attacks
02
Forward-Edge Integrity: Indirect Branch Tracking (IBT)
03
The #CP Fault: Exception 21
04
Backward-Edge Defense: Shadow Stacks
05
Signal Handling & Context Switching
06
The Kernel Interface: arch_prctl(2)
07
Edge Cases & Production Deployment
20-minute talk + 10-minute Q&A
2
Notes: Good morning everyone. Today I'm going to take you through a deep dive into Intel's Control-Flow Enforcement Technology and how it's implemented in the Linux kernel. We'll look at actual kernel source code, understand the hardware mechanisms, and see how the kernel handles all the tricky edge cases -- signals, fork, context switches -- that make this a fascinating piece of systems engineering.

## Slide 3
Why Hardware CFI?
The Problem: Code-Reuse Attacks
NX bit stopped code injection — attackers adapted
ROP — Return-Oriented Programming
Chains small "gadgets" ending in RET
Hijacks backward-edge (return addresses on stack)
JOP — Jump-Oriented Programming
Chains gadgets ending in JMP/CALL
Hijacks forward-edge (indirect branches)
Software mitigations (CFI, RAP) impose measurable runtime cost
The Solution: Intel CET
Control-flow Enforcement Technology
Silicon-level protection
Enforced by CPU microarchitecture — not software
Zero runtime overhead
Hardware checks happen in parallel with execution
Complete coverage
IBT protects forward-edge (JMP/CALL targets)
Shadow Stacks protect backward-edge (RET)
Transparent to well-behaved code
03
Notes: Let's start with why we need hardware CFI. Once we got NX -- non-executable stacks -- attackers couldn't inject shellcode anymore. So they adapted. Return-Oriented Programming chains tiny sequences of existing code that end in RET -- called gadgets -- to achieve arbitrary computation without ever injecting new code. Jump-Oriented Programming is the same idea but using indirect JMP and CALL instructions. Software defenses like retpolines and kCFI work but have performance costs. CET gives us silicon-level enforcement: the CPU itself checks control flow at every RET and every indirect branch, with essentially zero overhead in the common case.

## Slide 4
Intel CET — Two Pillars
IBT — Forward Edge
Indirect Branch Tracking
Restricts valid indirect branch targets
Only ENDBR64 instructions allowed as landing pads
Protects against JOP attacks
Fault: #CP with CP_ENDBR (error code 3)
Kernel support since Linux 5.18
GCC/Clang: -fcf-protection=branch
Shadow Stacks — Backward Edge
Hardware Return Address Stack
Parallel shadow stack maintained by CPU
CPU verifies RET address matches shadow copy
Protects against ROP attacks
Fault: #CP with CP_RET (error code 1)
Userspace support since Linux 6.6
GCC/Clang: -fcf-protection=return
Both share exception vector: #CP (Trap 21)
04
Notes: CET has two complementary mechanisms. IBT -- Indirect Branch Tracking -- is the forward-edge defense. It ensures that every indirect CALL or JMP lands on a valid target marked with an ENDBR instruction. It was merged for the kernel in Linux 5.18. Shadow Stacks are the backward-edge defense. The CPU maintains a second, read-only stack that stores only return addresses. On every RET, it compares both stacks. Userspace shadow stack support landed in Linux 6.6. Both mechanisms share a single exception vector -- trap 21, the Control Protection fault.

## Slide 5
Indirect Branch Tracking — How It Works
1
Indirect CALL/JMP
CPU executes an indirect
branch instruction
2
WAIT_FOR_ENDBRANCH
CPU sets internal tracker
state to "waiting"
3
Check Next Insn
CPU inspects the next
instruction at target
4
ENDBR64 Present
Valid landing pad — execution continues
Tracker reset, ENDBR consumed as NOP
5
No ENDBR — #CP Fault
Missing landing pad — CPU traps
Error code: CP_ENDBR = 3
Exception vector: #CP (Trap 21)
Key Details
ENDBR64 opcode: F3 0F 1E FA (encodes as REP NOP on older CPUs)
ENDBR32 opcode: F3 0F 1E FB (32-bit variant)
IBT is a "legacy compatible" feature:
ENDBR decodes as NOP on hardware without CET — binaries remain backward compatible
Controlled by CR4.CET and MSR_IA32_U_CET / MSR_IA32_S_CET
05
Notes: Here's how IBT works at the microarchitectural level. When the CPU executes an indirect CALL or JMP, it enters a state called Wait For ENDBRANCH. The very next instruction that executes must be an ENDBR64 instruction -- a specific four-byte opcode. If it is, the WFE state clears and execution proceeds normally. If it isn't, the CPU raises a CP fault with error code 3 -- CP_ENDBR. The compiler handles the emission: with cf-protection equals branch, GCC and Clang emit ENDBR at every function that could potentially be an indirect call target. The cost is just 4 bytes per valid target -- the ENDBR instruction itself is essentially a fancy NOP when executed sequentially.

## Slide 6
The ENDBR Lifecycle — Compile, Boot, Runtime
COMPILE TIME
gcc -fcf-protection=branch
ENDBR at every function entry
Too many — conservative
objtool --ibt
Finds functions only reached
by direct CALL
Records addresses in
.ibt_endbr_seal
Fewer valid targets
identified at build time
BOOT TIME
apply_seal_endbr()
For each addr in
.ibt_endbr_seal:
is_endbr(addr)?
uses gen_endbr() to verify
text_poke_early()
replaces with gen_endbr_poison()
0xd6401f0f
Sealed: jump here = #CP fault
RUNTIME
BPF JIT / V8 / LuaJIT
EMIT_ENDBR()
= EMIT(gen_endbr(), 4)
f3 0f 1e fa
Writes ENDBR64 into JIT'd code
so indirect calls to generated
code don't trigger #CP
JIT code = first-class IBT citizen
eBPF tail calls land on ENDBR
7
Notes: This slide shows the full ENDBR lifecycle across three phases. At compile time, GCC with fcf-protection equals branch emits ENDBR at every function entry. It's conservative because it can't always prove whether a function pointer exists. Then objtool, a build-time static analysis tool, walks the object files and finds functions that are only ever reached by direct CALL. It records their addresses in a special ELF section called dot ibt_endbr_seal. At boot time, apply_seal_endbr iterates that section. For each address, it verifies the instruction is actually ENDBR using gen_endbr, then replaces it with gen_endbr_poison -- the unique poison NOP, nopl minus 42 percent rax, opcode 0xd6401f0f -- via text_poke_early. After sealing, an indirect jump to those sites triggers a CP fault. But the story doesn't end at boot. JIT engines like BPF, V8, and LuaJIT generate code at runtime with indirect branch targets, so they must also emit ENDBR. The BPF JIT does this with EMIT_ENDBR, which calls gen_endbr to get the opcode and writes the raw bytes f3 0f 1e fa into the generated code buffer. Each phase corrects the previous one's limitations: GCC over-marks, objtool identifies the excess, the kernel seals them, and JIT engines extend the system to dynamically generated code.

## Slide 7
Generating ENDBR Without Embedding It
/* arch/x86/include/asm/ibt.h lines 44–57 */
#define gen_endbr() \
asm volatile( \
ALTERNATIVE( \
"mov $~0xfa1e0ff3, %[scratch]\n\t" \
"not %[scratch]\n\t", \
"", \
X86_FEATURE_IBT) \
: [scratch]
"=&r"
(__junk) \
: \
:
"memory"
);
/* On non-IBT CPUs: ALTERNATIVE patches to NOP */
/* On IBT CPUs: mov+not produces ENDBR64 opcode */
MOV loads bitwise NOT
~0xfa1e0ff3 = 0x05e1f00c
NOT flips bits back
NOT(0x05e1f00c) = 0xfa1e0ff3 = ENDBR64
Why not direct MOV?
Direct encoding would create ENDBR gadget in .text
"=&r" early-clobber
Scratch register written before inputs consumed
Byte Transformation in Memory
0x05e1f00c
→ NOT →
0xfa1e0ff3
→ decode →
ENDBR64
06
Notes: This is one of my favorite implementation details. When the kernel needs to compare an instruction against the ENDBR opcode at runtime -- for example, to check if a function starts with ENDBR -- it can't just do a mov with the literal value 0xfa1e0ff3. Why? Because those bytes -- f3, 0f, 1e, fa -- would appear contiguously in the instruction stream as the immediate operand. An attacker doing a jump-into-the-middle-of-an-instruction could land on those bytes and the CPU would interpret them as a valid endbr64, creating an unintended landing pad. So the kernel does something clever: it loads the bitwise NOT of the value -- which is a harmless constant -- and then flips it at runtime with a NOT instruction. The actual ENDBR opcode bytes never appear together in the binary. The early-clobber constraint tells GCC: this output register gets written before you're done reading inputs, so don't reuse the same register.

## Slide 8
Control Protection Exception — Error Codes
/* arch/x86/kernel/cet.c lines 8–18 */
enum
cp_error_code {
CP_EC =
BIT(15)
,
/* SGX enclave */
CP_RET =
1
,
/* near RET */
CP_IRET =
2
,
/* IRET/far RET */
CP_ENDBR =
3
,
/* missing ENDBR */
CP_RSTORSSP =
4
,
/* RSTORSSP token */
CP_SETSSBSY =
5
,
/* SETSSBSY token */
};
Key Error Codes
Code
Meaning
Protects
1
CP_RET
Shadow stack mismatch on RET
SHSTK
3
CP_ENDBR
Missing ENDBR at branch target
IBT
bit 15
CP_EC (CP_ENCL)
Fault occurred inside SGX enclave
Both
Exception Details
Vector 21 (#CP) — shared for all CET violations
Error code low bits identify the specific CET sub-feature
Bit 15 (CP_EC) is OR-ed in if fault originated from within an SGX enclave
Kernel handler dispatches based on error code to distinct recovery paths
08
Notes: The CP fault carries an error code that tells us exactly what went wrong. CP_RET means the return address from the normal stack didn't match the shadow stack -- a ROP attempt was just blocked. CP_ENDBR means an indirect branch landed somewhere without ENDBR -- a JOP attempt blocked. CP_RSTRORSSP and CP_SETSSBSY relate to shadow stack management instructions that failed validation. And bit 15 tells us if the fault happened inside an SGX enclave.

## Slide 9
Kernel #CP Handler — Routing Faults
/* arch/x86/kernel/cet.c lines 149–162 */
DEFINE_IDTENTRY_ERRORCODE
(exc_control_protection)
{
if
(!cpu_feature_enabled(X86_FEATURE_IBT)) {
pr_err(
"unexpected #CP\n"
);
BUG();
}
if
(user_mode(regs)) {
force_sig_fault(SIGSEGV, SEGV_CPERR,
(
void
__user *)regs->ip);
return
;
}
/* kernel-mode fault */
ibt_fatal = !sysctl_ibt_warn;
ibt_fatal = !sysctl_ibt_warn;
Dispatch Logic
User-mode #CP
Sends SIGSEGV with si_code = SEGV_CPERR
Process terminated — standard signal handling
Kernel-mode #CP
Default: BUG() — panic the kernel
ibt=warn: WARN() — log and continue
Boot param allows permissive mode for debugging
FRED-aware
Clears WFE (Wait-For-ENDBRANCH) state on entry
Handler Flow Summary
#CP trap → check IBT enabled → user_mode? → SIGSEGV : (ibt_warn? → WARN : BUG)
FRED (Flexible Return and Event Delivery) automatically manages the tracker state
09
Notes: Here's the actual exception handler. It's clean and straightforward. First check: are we coming from user mode or kernel mode? User-mode CP means a shadow stack violation -- the process tried to RET to a tampered address. The kernel delivers SIGSEGV with the new signal code SEGV_CPERR. Kernel-mode CP means an IBT violation -- an indirect branch in kernel code landed on a non-ENDBR instruction. By default that's a BUG -- you can soften it to a WARN with the ibt equals warn boot parameter for debugging. There's one special case for FRED-aware CPUs: newer Intel processors preserve the WFE state across exception delivery, so we have to explicitly clear it.

## Slide 10
Hardware Shadow Stack — The Mechanism
Normal Stack
(read/write)
local vars, args
return addr
saved RBP
...
Shadow Stack
(read-only)
return addr
return addr (prev frame)
...
CALL
pushes to BOTH
RET
pops + compares
Match = Continue
Mismatch = #CP
Critical Properties
Shadow stack is NOT writable by normal MOV/PUSH instructions
Only CALL, RET, and special CET instructions (WRSS, INCSSP) modify it
MSR_IA32_PL3_SSP holds the current user Shadow Stack Pointer
Mismatch on RET triggers #CP with error code CP_RET = 1
MSR_IA32_PL3_SSP = 0x000006A4 MSR_IA32_U_CET = 0x000006A0
10
Notes: The shadow stack concept is beautifully simple. The CPU maintains two stacks in parallel. When CALL executes, it pushes the return address to both the normal stack and the shadow stack. When RET executes, it pops from both and compares. If they match -- normal execution. If they don't -- CP fault, code CP_RET. The critical property: the shadow stack is not writable by normal memory instructions. You cannot MOV or PUSH to it. Only CALL and RET can modify it through normal operation. There's also WRSS -- a special instruction that can write to the shadow stack -- but that requires explicit opt-in, and we'll see why that matters for setjmp.

## Slide 11
Enabling Shadow Stacks — shstk_setup()
// arch/x86/kernel/shstk.c, lines 149-177
static int shstk_setup(void)
{
struct thread_shstk *shstk =
&current->thread.shstk;
unsigned long addr, size;
if (features_enabled(ARCH_SHSTK_SHSTK))
return 0; /* already enabled */
size = adjust_shstk_size(0);
addr = alloc_shstk(0, size, 0, false);
fpregs_lock_and_load();
wrmsrq(MSR_IA32_PL3_SSP, addr + size);
wrmsrq(MSR_IA32_U_CET, CET_SHSTK_EN);
fpregs_unlock();
shstk->base = addr;
shstk->size = size;
features_set(ARCH_SHSTK_SHSTK);
return 0;
}
Size allocation
min(RLIMIT_STACK, 4GB), page-aligned
MAP_ABOVE4G
Prevents 32-bit address aliasing attacks
SSP at top
addr + size (stacks grow downward)
Guard page protection
INCSSP max reach = 2040 bytes
Guard page = 4096 bytes > max reach
Memory Layout
guard page (4096B)
shadow stack (grows down)
SSP starts here (top)
11
Notes: Here's shstk_setup -- the function that enables shadow stacks for the current thread. First it allocates the shadow stack memory. The size defaults to the minimum of RLIMIT_STACK and four gigabytes, page-aligned. A key detail: MAP_ABOVE4G ensures the allocation is above the four-gigabyte boundary, preventing 32-bit address aliasing attacks. Then we write the MSRs: PL3_SSP gets set to the top of the allocated region because stacks grow downward, and U_CET gets the shadow stack enable bit set. The guard page detail is important -- INCSSP can advance the shadow stack pointer by at most 2040 bytes per instruction, and a 4096-byte guard page guarantees that any attempt to slide into an adjacent shadow stack will fault.

## Slide 12
Signals vs. Shadow Stacks
The Problem
1. Signal delivery diverts control flow to handler
2. Handler returns via sa_restorer trampoline (RET)
3. Shadow stack expects the original caller's return address
4. Without fixup: #CP fault on every signal return
Signal Delivery Protocol (Solution)
Step 1
Push sigframe token
old_ssp | BIT(63)
Step 2
Push sa_restorer
onto shadow stack
Step 3
Update SSP
MSR_IA32_PL3_SSP
Step 4
Handler's RET
matches sa_restorer
Step 5
rt_sigreturn validates token
restores original SSP
Security: BIT(63) ensures token can never match a RET address — attacker cannot forge tokens without WRSS or kernel access
restore_signal_shadow_stack() reverses the entire protocol on sigreturn
12
Notes: This is where it gets tricky. When a signal arrives, the kernel diverts execution to the signal handler. The handler eventually returns via a trampoline that calls rt_sigreturn. But here's the problem: that return goes through a RET instruction, and the shadow stack still has the original caller's return address -- not the trampoline's address. Without a fixup mechanism, every single signal return would trigger a CP fault. The solution is elegant: during signal delivery, the kernel pushes a special sigframe token onto the shadow stack -- the original SSP with bit 63 set. Bit 63 means this is not a return address -- the CPU will never match it. Then it pushes the sa_restorer address so the handler's RET will match. On sigreturn, the kernel validates the token and restores the original SSP.

## Slide 13
setup_signal_shadow_stack()
// arch/x86/kernel/shstk.c, lines 384-416
int setup_signal_shadow_stack(
struct ksignal *ksig)
{
void __user *restorer =
ksig->ka.sa.sa_restorer;
unsigned long ssp;
ssp = get_user_shstk_addr();
/* Push sigframe token:
* old_ssp | BIT(63) */
shstk_push_sigframe(&ssp);
/* Push restorer so handler's
* RET matches */
ssp -= SS_FRAME_SIZE;
write_user_shstk_64(
(u64 __user *)ssp,
(u64)restorer);
fpregs_lock_and_load();
wrmsrq(MSR_IA32_PL3_SSP, ssp);
fpregs_unlock();
return 0;
}
SHSTK_DATA_BIT (bit 63)
Ensures token can never match
a legitimate RET address
sa_restorer
= __restore_rt
Calls rt_sigreturn syscall
Reverse on sigreturn
restore_signal_shadow_stack()
Validates token, restores original SSP
Shadow Stack State During Signal
sa_restorer addr (top, SSP here)
sigframe token (old_ssp | BIT(63))
original return addresses...
13
Notes: Here's the actual code. setup_signal_shadow_stack is called during signal delivery, after the signal frame is constructed on the normal stack. It reads the current SSP, then pushes a restore token -- the old SSP OR'd with SHSTK_DATA_BIT, bit 63. Then it pushes the restorer address -- that's the __restore_rt trampoline in the vDSO -- so when the signal handler does its final RET, it matches. Finally it updates the SSP MSR to the new position. On the way back, restore_signal_shadow_stack reverses everything: validates the token, checks it's on a shadow stack VMA, and restores the original SSP.

## Slide 14
Shadow Stack Lifecycle — Fork, Threads, vfork
// arch/x86/kernel/shstk.c, lines 186-226 (simplified)
unsigned long shstk_alloc_thread_stack(
struct task_struct *tsk,
u64 clone_flags,
unsigned long stack_size)
{
if (clone_flags & CLONE_VFORK) {
shstk->base = 0;
/* share parent's */
shstk->size = 0;
return 0;
}
if (!(clone_flags & CLONE_VM))
return 0; /* fork: COW */
/* pthread_create: new stack */
size = adjust_shstk_size(stack_size);
addr = alloc_shstk(0, size, 0, false);
shstk->base = addr;
shstk->size = size;
return addr + size;
}
Scenario
Flags
Action
fork()
!CLONE_VM
COW copy
(free)
vfork()
CLONE_VFORK
Share parent's
base=0, size=0
pthread_create()
CLONE_VM
Allocate new
returns addr+size
Why base=0 for vfork?
Prevents shstk_free() from unmapping the parent's shadow stack
Returned SSP is stored into child's XSAVE area by update_fpu_shstk()
Child resumes with correct shadow stack pointer on first context switch
14
Notes: Shadow stack behavior during process creation has three cases. For fork -- no CLONE_VM -- the child gets a copy-on-write copy of the parent's shadow stack. This is free -- normal COW page fault handling duplicates pages on write. For vfork -- CLONE_VFORK -- the child temporarily shares the parent's shadow stack. We set base and size to zero so shstk_free won't accidentally unmap the parent's stack when the child exits. For pthread_create -- CLONE_VM -- the child shares the address space, so it needs its own shadow stack. We allocate a fresh one and return the new SSP pointing to the top.

## Slide 15
SSP During Context Switch
// arch/x86/kernel/fpu/core.c, lines 634-658
static int update_fpu_shstk(
struct task_struct *dst,
unsigned long ssp)
{
struct cet_user_state *xstate;
if (!ssp)
return 0;
xstate = get_xsave_addr(
&x86_task_fpu(dst)
->fpstate->regs.xsave,
XFEATURE_CET_USER);
xstate->user_ssp = (u64)ssp;
return 0;
}
XFEATURE_CET_USER
SSP stored in XSAVE area under this feature
Context switch: automatic
XSAVE saves outgoing, XRSTOR loads incoming SSP
Zero scheduler overhead
No explicit MSR read/write in fast path
fpu_clone()
Calls update_fpu_shstk() to set child's initial SSP
Context Switch Flow
Task A (outgoing)
SSP in registers
XSAVE
XSAVE Buffer
CET_USER.ssp
XRSTOR
Task B (incoming)
SSP restored
15
Notes: The shadow stack pointer lives in the XSAVE area under XFEATURE_CET_USER. This is elegant: during a context switch, the normal XSAVE instruction saves the outgoing task's SSP, and XRSTOR on the incoming task loads its SSP. No special code needed in the scheduler fast path. The only time we explicitly touch the SSP in the XSAVE buffer is during fpu_clone -- when we need to set the child's initial SSP to point to its newly allocated shadow stack.

## Slide 16
Userspace Control — arch_prctl(2) for CET
// arch/x86/include/uapi/asm/prctl.h
#define ARCH_SHSTK_ENABLE 0x5001
#define ARCH_SHSTK_DISABLE 0x5002
#define ARCH_SHSTK_LOCK 0x5003
#define ARCH_SHSTK_UNLOCK 0x5004
#define ARCH_SHSTK_STATUS 0x5005
#define ARCH_SHSTK_SHSTK (1ULL << 0)
#define ARCH_SHSTK_WRSS (1ULL << 1)
// Usage pattern
/* Enable shadow stack */
arch_prctl(ARCH_SHSTK_ENABLE,
ARCH_SHSTK_SHSTK);
/* Lock -- prevents disabling */
arch_prctl(ARCH_SHSTK_LOCK,
ARCH_SHSTK_SHSTK);
LOCK
Prevents disable even by the process itself
Attacker with code execution cannot call DISABLE
UNLOCK
Only via ptrace (for CRIU/checkpoint-restore)
External debugger privilege required
glibc auto-enable
CET-compiled binaries with GNU property notes:
Dynamic linker enables + locks before main()
Production Escape Hatch
GLIBC_TUNABLES=glibc.cpu.hwcaps=-SHSTK ./app
Per-process, no kernel restart needed — useful for legacy apps and incompatible JITs
16
Notes: Userspace controls shadow stacks through arch_prctl. ENABLE turns it on -- calls shstk_setup that we just saw. DISABLE turns it off -- zeroes the MSR, unmaps the shadow stack. The critical one is LOCK. Once you lock a feature, the process cannot disable it -- even if an attacker gains arbitrary code execution and tries to call arch_prctl with DISABLE. UNLOCK is only available via ptrace -- this is for checkpoint and restore scenarios. In practice, glibc handles all of this: when loading a binary with CET GNU property notes, the dynamic linker enables and locks shadow stacks before main runs. For production deployments where you need to disable CET for specific applications, GLIBC_TUNABLES provides a per-process escape hatch without any kernel changes.

## Slide 17
Edge Cases & Deployment
setjmp / longjmp
Problem:
longjmp skips intermediate
frames, shadow stack has
stale entries
Solution:
glibc uses INCSSP
to advance past stale entries
Deep longjmp:
May require WRSS
(separate opt-in via
arch_prctl)
JIT Engines
V8, LuaJIT, eBPF
Must emit ENDBR at all
generated indirect targets
map_shadow_stack
Syscall for custom coroutine
and fiber shadow stacks
eBPF JIT:
Tail calls must land on
ENDBR instruction
GLIBC_TUNABLES
glibc.cpu.hwcaps=
-SHSTK
Disables shadow stacks
at dynamic linker level
Benefits:
+ Per-process control
+ No kernel restart
+ Legacy app support
+ Debugging use cases
17
Notes: Three important edge cases. First, setjmp and longjmp: when you longjmp back, the shadow stack has stale entries from the intermediate calls. Glibc's longjmp implementation uses INCSSP to advance past those entries. For particularly deep longjmps, WRSS might be needed -- that's why it's a separate opt-in feature. Second, JIT engines: any JIT that generates code with indirect branches -- V8, LuaJIT, eBPF -- must emit ENDBR at all generated targets. The map_shadow_stack syscall lets JIT engines allocate shadow stacks for custom coroutines or fibers. Third, for production deployment, GLIBC_TUNABLES is your escape hatch. Set glibc.cpu.hwcaps equals minus SHSTK and the dynamic linker skips enabling shadow stacks for that process. No kernel restart, no system-wide impact.

## Slide 18
Summary & Timeline
Linux 5.18
May 2022
Kernel IBT
Linux 6.4
Jun 2023
FineIBT
Linux 6.6
Oct 2023
User Shadow Stacks
Linux 6.6+
Ongoing
map_shadow_stack
Key Takeaways
1.
CET delivers hardware CFI with zero performance tax on the fast path
2.
IBT protects forward edges — ENDBR validation, sealing, and #CP enforcement
3.
Shadow Stacks guard backward edges — read-only return addresses + signal tokens
4.
Production-ready: glibc integration, arch_prctl locking, GLIBC_TUNABLES
5.
Entire implementation lives files under arch/x86/
Questions?
Jay Tharwani
jtharwan@alumni.uncc.edu
Scan for slides
18
Notes: To summarize: CET gives us hardware control-flow integrity at zero cost on the fast path. IBT handles the forward edge with ENDBR plus sealing. Shadow stacks handle the backward edge with a read-only return address stack and a clever signal token protocol. The kernel interface is clean: arch_prctl with locking for security, GLIBC_TUNABLES for flexibility. And remarkably, the entire implementation lives in about five files under arch/x86. We've come a long way from the initial IBT merge in 5.18 to full userspace shadow stack support in 6.6 -- and it's production-ready today on 12th-gen Intel and newer. Thank you -- I'm happy to take questions.